## Slide 1: Development Environment and Software
Arduino IDE. Sketch. Functions. Debugging
Software University
https://softuni.bg
SoftUni Team
Technical Trainers

## Slide 2: Table of Contents
Arduino IDE
Sketch
Basic Arduino IDE Functions
  Basic Functions. Variables. Libraries
Debugging and Serial Communication
  Serial Monitor
Examples

## Slide 3: Arduino IDE
Introduction. Main View. Toolbar

## Slide 4: Arduino IDE
Arduino Integrated Development Environment (IDE) is used to write and upload programs to Arduino compatible boards
  Supports the languages C and C++
Start with Arduino IDE:
  Download and install from: https://www.arduino.cc/en/software
  Install needed Board Manager library and select your board
  Select the correct COM port for the board
Note: for detailed instructions read the provided guidelines!

## Slide 5: Select Your Board: NodeMCU 1.0

## Slide 6: Select the Correct COM Port

## Slide 7: Arduino IDE – Main View
Sketch name
Arduino IDE version
Menus
Toolbar buttons
Code area
Upload status message
Messages from the system
Configured board and COM port

## Slide 8: Toolbar Buttons
Verify – check the code for errors
Upload – compile and upload the code to the board
New – create a new sketch
Open – open a saved sketch
Save – save the sketch
Serial Monitor – display serial data sent from the board

## Slide 9: Sketch
Structure. Creating a Sketch

## Slide 10: Sketch - Structure
The Sketch is the main code (program), created in Arduino IDE
  Generates a Hex File which is uploaded on the board
  Requires two basic functions:
void setup() {
// Initialization of variables, pin modes, libraries
// Runs only once after each power up or reset
}
void loop() {
// Loops the code consecutively
}

## Slide 11: Creating a Sketch
Edit
Verify
Upload
Create new or open an existing sketch
Edit here
Save the sketch
Verify if the sketch is compiling
Upload the sketch on the microcontroller

## Slide 12: Arduino Examples
Arduino IDE has built-in code samples in Examples section:

## Slide 13: Opening Sketch – "Blink" Example

## Slide 14: Compiling the "Blink" Example

## Slide 15: Uploading the "Blink" Example

## Slide 16: The "Blink" Example in Action

## Slide 17: Basic Arduino IDE Functions
Basic IDE Functions. Variables. Libraries

## Slide 18: Hardware Related Functions
pinMode() – setup the I/O functions of hardware pins
digitalWrite() – set a pin to a digital level
digitalRead() – return the given pin value
delay() – pause for the given milliseconds
pinMode(2, OUTPUT)
digitalWrite(16, HIGH) / digitalWrite(D0, HIGH)
delay(1000) // pause for 1 second
digitalRead(16) / digitalRead(D0)
pinMode(D4, INPUT)

## Slide 19: Flow-Control: If-Else, For, Do-While
Examples:
if (x > 120) {
digitalWrite(13, HIGH);
} else {
digitalWrite(13, LOW);
}
for (int i = 0; i <= 255; i++) {
analogWrite(PWMpin, i);
delay(10);
}
do {
delay(50);
x = readSensors();
} while (x < 100);
for loop
if – else construction
do-while

## Slide 20: Variables
Variables – used for storing data (from sensors or a calculation)
Declaring variable – define its type and (optionally) set an initial value (initialize the variable)
Rollover – when variables exceed their maximum capacity, they "roll over" back to their minimum capacity and vice versa
int onboardLED = 16;
byte x;
x = 0;
x = x - 1; // x = 255
byte x;
x = 255;
x = x + 1; // x = 0
byte brightness = 13;

## Slide 21: Variable Types
Type | Value Range | Size (Bytes)
boolean | True or False | 1
char | -128 to 127 | 1
byte | 0 to 255 | 1
int | -32768 to 32767 | 2
unsigned int | 0 to 65535 | 2
long | -2147483648 to 2147483647 | 4
unsigned long | 0 to 4294967295 | 4
float | -3.4028235E+38 to 3.4028235E+38 | 4
double | -3.4028235E+38 to 3.4028235E+38 | 4
String | Character array | -

## Slide 22: Libraries
Libraries provide extra functionality for use in sketches:
  To connect with sensors
  To manipulate data, etc.
Use a library from:
  Sketch > Include Library
  #include<> statement will be added to the sketch
#include <Servo.h>

## Slide 24: Debugging and Serial Communication
Serial Monitor

## Slide 25: Debugging
Debugging in Arduino IDE is complicated
  The code depends on outputs / inputs of a physical device
Debugging a sketch includes:
  Checking the hardware:
    wires, components, etc.
  Trying to compile the code
    Look for syntax errors
  Code debugging with Serial Monitor:
    Read data from the device at each code step

## Slide 26: Serial Monitor
Serial Monitor displays messages sent from the microcontroller
Serial communications allow the microcontroller to interact with the computer and other devices
  Serial.begin(baud rate) – start serial communication
    baud rate – maximum transferred bits per second
  Serial.println("{message}") – print message from the board
  Serial.read() – read command from Serial Monitor
  Serial.end() – close serial connection

## Slide 27: Serial Communication – Example
void setup() {
Serial.begin(9600);
}
void loop() {
Serial.println("Hello world!");
delay(1000);
}
Baud rate in the code
Set the same baud rate in the IDE

## Slide 28: Serial.println(): Printing Text + Number
void setup() {
Serial.begin(9600);
}
void loop() {
for (int i=1; i<=100; i++) {
// This will fail!
Serial.println("i = " + i);
// Use: print("i = "); println(i);
delay(1000);
}
}

## Slide 29: tinkercad.com
Online Arduino Simulator

## Slide 30: Tinkercad
Easy-to-use app for 3D design, electronics and coding
After registration, you can:
  watch lessons with examples
  build virtual circuits
  run your Arduino sketch on the virtual Arduino board
    NodeMCU ESP-12E is not supported!
  There is real sketch Debugger!

## Slide 31: Tinkercad Simulator
Choose wire type and color
Paste your sketch
Start simulation
Search for circuit components
Drag and position the components here

## Slide 32: Tinkercad Simulator – Example

## Slide 33: Tinkercad Simulator – Debugger
Read the debugger instructions
Buttons for pause and step over lines
Breakpoint on line 6
ledValue = 0
Use the button to go through the loop() method
ledValue = 1

## Slide 34: Examples

## Slide 35: Internal LED Blink
Make the blue internal LED blink by keeping it ON for 1 seconds and OFF for 2 second
  Warning: NodeMCU ESP-12E module has 2 build-in LEDs – on GPIO 2 and GPIO 16 (find the one, shown on the picture)
  Connect the module to the computer and configure Arduino IDE to the correct COM port
  Write the code
  Verify if the code is compiling
  Upload the sketch to the board
Note: The internal LED is ON on LOW voltage and OFF on HIGH voltage

## Slide 36: Internal LED Blink – Solution
You can load sample code from: File > Examples > ESP8266 > Blink
In the example is used the built-in variable LED_BUILTIN, which is on GPIO2
In this case we use the LED on GPIO16
void setup() {
pinMode(16, OUTPUT);
}
void loop() {
digitalWrite(16, LOW);
delay(1000);
digitalWrite(16, HIGH);
delay(2000);
}

## Slide 37: Double Blink
Make the Built-in and the Onboard internal LEDs blink together
  First turn them ON and then OFF on 2 seconds intervals
  After each blink reduce the interval with 50 ms
  When the interval becomes 100 ms, begin again from 2 s

## Slide 38: Double Blink – Solution
void loop() {
while (interval > 100) {
digitalWrite(LED1, LOW);
digitalWrite(LED2, LOW);
delay(interval);
digitalWrite(LED1, HIGH);
digitalWrite(LED2, HIGH);
delay(interval);
interval = interval - 50;
}
interval = 2000;
}
int LED1 = 2;
int LED2 = 16;
int interval = 2000;
void setup() {
pinMode(LED1, OUTPUT);
pinMode(LED2, OUTPUT);
}

## Slide 39: External LED Blink
Use the diagram to create a circuit with an external LED
  Use 100 Ohm resistor or higher
Program the LED to turn ON and OFF every 0.5 s
After every fifth blink turn OFF the LED for 2 s instead of 0.5 s

## Slide 40: External LED Blink – Solution
void loop() {
blinkCounter++;
digitalWrite(LED, 1);
delay(500);
digitalWrite(LED, 0);
if (blinkCounter % 5 == 0) {
delay(2000);
} else {
delay(500);
}
}
int LED = D7; // GPIO 13
int blinkCounter = 0;
void setup() {
pinMode(LED, OUTPUT);
}

## Slide 41: Summary
…
…
…
Arduino IDE is software for programming microcontroller boards
  It needs to be configurated for the NodeMCU ESP-12E module
  On each connection the COM port of the device should be checked
Sketch is the main program, uploaded to the board. It needs 2 main methods:
  void setup() – runs only once at the beginning
  void loop() – runs repeatedly
Arduino IDE has build-in libraries and functions for programming controllers:
  pinMode(), digitalRead(), digitalWrite(), delay()…
The main code debugging method is by using Serial Communication and checking the messages in the Serial Monitor tool. Commands for serial communication:
  Serial.begin(), Serial.println(), Serial.end()

## Slide 42: Questions?

## Slide 43: License
This course (slides, examples, code, demos, exercises, tutorials, homework, projects, documents, videos and other assets) is copyrighted content, created by SoftUni
Unauthorized copy, reproduction or use is illegal
© SoftUni – https://softuni.org
© Software University – https://softuni.bg